## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Chart: Statistical Alarm Plot
Chart: Correlation Coefficient Pump Failure (1 or 0) - Rolling Standard Deviation (30 Minute)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
Correlation Coefficient | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Chart: DRT Rolling Standard Deviation
Chart: DRT Rolling Mean

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through box & whisker plots show a clear signature difference between that of normal behaviour and that of Failure with pump torque, pump speed (RPM), and Pump Efficiency showing the 3 largest variances.

## Slide 4: Correlation analyses across datasets yield interesting insights with Pump Speed (RPM), Volumetric Flow Meter 1, and Pump Efficiency negatively correlated with Pump Failure in the Rolling Mean Data, whilst Horse Power, Volumetric Flow Meter 1, and Pump Efficiency show a subsequently strong positive correlation in the Rolling Standard Deviation Dataset.
Chart: Correlation Strength Associated with Pump Failure (Raw Data)
Horse Power | 0.42184
Pump Speed (RPM) | 0.26001
Pump Torque | 0.23318
Ambient Temperature | 0.20801
Pump Efficiency | -0.10268
Volumetric Flow Meter 1 | -0.10249
Volumetric Flow Meter 2 | -0.11211
Chart: Correlation Strength Associated with Pump Failure (Rolling Standard Deviation)
Horse Power | 0.6901
Volumetric Flow Meter 1 | 0.64488
Pump Efficiency | 0.64355
Volumetric Flow Meter 2 | 0.62592
Pump Speed (RPM) | 0.62456
Ambient Temperature | 0.60005
Pump Torque | 0.59726
Chart: Correlation Strength Associated with Pump Failure (Rolling Mean)
Horse Power | 0.21803
Pump Speed (RPM) | -0.18417
Pump Torque | -0.21603
Ambient Temperature | -0.30265
Volumetric Flow Meter 1 | -0.69244
Pump Efficiency | -0.69503
Volumetric Flow Meter 2 | -0.69773

## Slide 5: Lastly, analysis of the model fit reveals that with a R Squared of 0.78, a linear model is a good fit for the data with variables Horse Power, Volumetric Flow Meter 2, and Pump Efficiency having the largest coefficients, indicative that these variables have the most immediate relationship with respect to Pump Failure behaviour.
Chart: Coefficient Ranking
| Horse Power | Pump Efficiency | Volumetric Flow Meter 1 | Ambient Temperature | Pump Speed (RPM) | Pump Torque | Volumetric Flow Meter 2
 | 0.76485 | 0.34237 | 0.050934 | 0.018207 | -0.017867 | -0.018902 | -0.61136